Workshop Tutorials for Physics

TR6: Heat Engines

A.  Qualitative Questions:

- We use heat engines all the time. A refrigerator uses a heat engine, as does an air conditioner. A car engine is also a type of heat engine.

  - Draw a schematic energy flow diagram for a heat engine. Label the hot and cold reservoirs.  Use arrows to show the transfer of energy QH, QC and W.

Consider a car engine.

  - What represents the hot and cold reservoirs, and the transfer of energy QH, QC and W?

  - Where in the engine does the cyclic thermodynamic process occur?

  - What is the working substance of the engine?

- With the cost of fuel constantly increasing, it is important that engines be as efficient as possible.

  - What limits the efficiency of an engine?

  - Why are diesel engines more efficient than petrol engines?

  - How could you go about increasing the efficiency of an engine? What drawbacks might this have?

B.  Activity Questions:

### Stirling engine

Examine the Stirling engine and compare the up and down strokes of the engine to the four stages of the Stirling cycle on the schematic below. Draw p-V diagrams for the four stages.

### Bar Fridge

Inspect the back of the bar fridge.

Identify the heat reservoirs.

Draw an energy flow diagram for fridge.

Could you cool a room by leaving the fridge door open?

# C. Quantitative questions.

- Air is mostly a mixture of diatomic oxygen and nitrogen which can be approximated as an ideal gas with ( = 1.40 and Cv = 20.8 J.mol-1.K-1. The compression ratio of a diesel engine is 15 to 1; this means that air in the cylinders is compressed to 1/15 of its initial volume.

If the initial pressure is 1.01 ( 105 Pa and the initial temperature is 27°C (300K), find

- the final temperature after compression,

- the final pressure after compression.

- How much work does the gas do during the compression if the initial volume of the cylinder is 1.00 L = 1.00 (10-3 m3?

- Brent is making some ice cubes for a cocktail party. He pours 2 litres of water at 15oC into ice cube trays and puts them in the freezer.

  - How much thermal energy must be removed from the water to freeze it into ice cubes?

Brent’s freezer has a coefficient of performance of 4.8.

  - How much energy does the freezer use to freeze the water?

  - Would the freezer make the ice cubes more quickly if the coefficient of performance were larger, say 5.0 instead of 4.8?

data:

R= 8.315 J.mol-1.K-1

density of water = 1 kg.l-1

heat capacity of water = 4.18 kJ.kg-1.K-1

latent heat of freezing = 333.5 kJ.kg-1

# Text boxes

gas flow

QH

TC

TC

TC

TC

TH

TH

TH

TH

QC

gas flow

1. expansion stroke

2. constant volume

3. compression stroke

4. constant volume